| MODEL SPS-70 DL DIGITAL POSTAL SCALE | User Manual Revision 1 April 29, 2009 |
| --- | --- |

©Transcell Technology, Inc. 2009. All rights reserved.

The information contained herein is the property of Transcell Technology and is supplied without liability for errors or omissions. No part may be reproduced or used except as authorized by contract or other written permission. The copyright and the foregoing restriction on reproduction and use extend to all media in which the information may be embodied.

Contents subject to change without notice.

|  | THIS EQUIPMENT CONTAINS NO USER SERVICEABLE COMPONENTS. Servicing of the equipment must only be carried out by trained and authorized personnel. Use only the AC adapter supplied with the scale. Other adapters may cause damage. |
| --- | --- |
|  | Routine maintenance Harsh abrasives, solvents, scouring cleaners and alkaline cleaning solutions should not be used; especially on the display window. The outside of the product may be wiped down with a clean cloth, moistened with water containing a small amount of soap. |

Installation

- Ensure that the scale is placed securely on a flat and level surface.

- Avoid installing the scale in areas of direct sunlight and high humidity. Also avoid drafts, vibrations and dusty conditions.

- To extend the life of your digital scale, do not drop items to be weighed onto the platform or overload the scale beyond its rated capacity. Shock-loading and overloading may damage the load cell and void the warranty.

Federal Communications Commission (FCC) Statement

This equipment has been tested and found to comply with the limits for a Class A digital device, pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses and can radiate radio frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the separation between the equipment and receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

- Consult the dealer or an experienced radio / TV technician for help.

“CE” logo here somewhere…

TABLE OF CONTENTS

Page

Chapter 1:	Introduction to the Transcell Model SPS-70DL Rate Computing Scale		1-1

Chapter 2:	Getting Started		2-1

Chapter 3:	Basics of Operation		3-1

3.1	Display		3-1

3.2	Keyboard		3-1

3.2.1	USPS, UPS and FedEx Rate Keys		3-1

3.2.1.1	USPS Rate Keys		3-1

3.2.1.2	UPS Rate Keys		3-2

3.2.1.3	FedEx Rate Keys		3-2

3.2.2	Operator Keys		3-2

3.2.2.1	Special Service Keys		3-2

3.2.2.2	ZIP/Zone Key		3-3

3.2.2.3	Clear (No) Key		3-3

3.2.2.4	Zero Key		3-3

3.2.2.5	Enter (Yes) Key		3-3

3.2.3	Function Keys		3-3

3.2.3.1	Star (*) Key		3-3

3.2.3.2	Piece Count Key		3-3

3.3	General Scale Operation		3-4

3.3.1	System Prompts		3-4

3.3.2	Mailing or Shipping an Item		3-4

3.3.3	Weighing a Letter or Package		3-4

3.3.4	Selecting a Class of Service		3-4

3.3.5	Entering a ZIP Code or Country Code		3-5

3.3.5.1	ZIP Code Entry		3-5

3.3.5.2	Country Code Entry		3-5

3.3.6	Selecting Special Services		3-5

Chapter 4:	Examples of Operation		4-1

4.1	Sending a Letter or Parcel by USPS First Class/Priority Mail		4-1

4.2	Sending an International Air Letter by USPS		4-2

4.3	Sending a Letter by UPS Second Day Air		4-3

4.4	Sending a Letter by Federal Express Standard Overnight		4-4

Chapter 5:	Advanced Features and Operation		5-1

5.1	Programmable Favorite Keys 	 5-1

5.2	How to Add and Remove Countries from the Favorites List	 5-1

5.3	Piece Counting 	 5-1

5.4	Hold Mode	 5-1

Chapter 6:	Setup Operations		6-1

6.1	Setup Operation Overview		6-1

6.2	Setup Menu		6-1

6.2.1	Origination ZIP code		6-1

6.2.2	Handling Charge		6-1

6.2.3	Buzzer Enable/Disable		6-2

6.3	Calibration Menu		6-2

6.4	ADC Diagnostic Menu		6-2

Chapter 7:	Legal for Trade Sealing		7-1

7.1	Sealing Method		7-1

Appendix A:	Specifications		A-1

Appendix B:	Standard Rates, Special Services and Functions		B-1

B.1	Standard Rates, Special Services and Functions		B-1

B.1.1	United States Postal Service (USPS)		B-1

B.1.2	United Parcel Service (UPS)		B-1

B.1.3	Federal Express (FEDEX)		B-1

B.1.4	Special Services		B-1

B.1.5	Functions		B-1

Appendix C:	Rate and Special Service Abbreviations		C-1

C.1	Rate Abbreviations		C-1

C.2	Special Services Abbreviations		C-1

Appendix D:	Country Code Chart		D-1

Appendix E:	Country Name Abbreviations		E-1

Appendix F:	Rate Change Information		F-1

Appendix G:	Error Messages		G-1

G.1	Error Messages		G-1

G.1.1	Operator Errors		G-1

Appendix H:  Rate Matrix	 H-1

LIST OF FIGURES

1-1	SPS-70DL Front Panel		1-1

2-1	SPS-70DL Back Panel		2-1

3-1	SPS-70DL Display Detail		3-1

3-2	Rate Keys and Operator Keys Layout		3-1

7-1	SPS-70DL Back Panel		7-1

# CHAPTER 1:  INTRODUCTION TO THE TRANSCELL MODEL SPS-70DL POSTAL COMPUTING SCALE

The Transcell Model SPS-70DL Digital Postal Computing Scale is designed for low volume mailroom shipping applications.  It is equipped with many helpful features that guide the operator through the day to day mailing activities.

The Model SPS-70DL has a maximum weighing capacity of 70 pounds.

Prior to using the scale, please read this user’s guide carefully and completely.  Store the manual in a safe and convenient place so it will be available if you have questions concerning the operation of the scale.

FIGURE 1-1: SPS-70DL Front Panel

# CHAPTER 2:  GETTING STARTED

After unpacking the scale, a small amount of preparation is required before the scale can be used for mailing or shipping.  Please refer to Figure 2-1 below as needed.

Figure 2-1: SPS-70DL Back Panel

Step 1.	Position the scale in its area of intended use. Observe the following guidelines for suitable location.

- Choose a firm, stable floor or table.

- Do not share an AC outlet with electrical noise producing equipment, such as refrigeration units. This includes products with electrical motors and/or relays.

- Do not place the scale in an area with changing ambient temperature and/or high humidity.

- Do not place the scale in an area prone to exposure to direct sunlight, wind, or dust.

- Do not place the scale in an area with vibrating equipment.

Step 2.	Install the AC Adapter.

1.	After placing the scale in its area of use, locate the Model A41408 AC Adapter.

2.	Connect the female end of the AC Adapter to the connector on the rear of scale, and then plug the adapter into an AC outlet.

Step 3.	Turn the scale’s AC power on to begin the initialization.

Step 4.	Initialization - The first time the scale is turned on you will be required to enter your origin ZIP Code.

1.	When the AC power switch is placed “ON” position, the scale prompts for your “origin ZIP Code”.

2.	Enter the first three digits of your ZIP Code.  The scale displays the ZIP Code entered and prompts you to verify (Yes or No) if the ZIP Code displayed is correct.

3.	If the ZIP Code is correct, press the “Yes” (Enter) key to complete the initialization or if the ZIP Code is incorrect, press the “No” (Clear) key and enter the correct ZIP Code.

# CHAPTER 3:  BASICS OF OPERATION

3.1	DISPLAY

The display is an LCD (Liquid Crystal Display) display capable of displaying the various system messages and information.

FIGURE 3-1: SPS-70/SPS-150 Display Detail

As shown in Figure 3-1, the scale displays the class of mail, weight, shipping charge (rate) and destination zone or country. When additional information is needed, the scale will prompt for the information.

3.2	KEYBOARD

The keyboard is composed of rate keys, operator keys and function keys. Refer to Figure 3-2 for the overall layout and key locations.

FIGURE 3-2: Rate Keys and Operator Keys Layout

3.2.1	USPS, UPS AND FEDEX RATE KEYS

The following key allows the access to the USPS rates, UPS rates and the Federal Express rates on the scale keyboard. In each case, pressing carrier key will prompt you to choose from one of the three major carriers.

      - USPS Rate Keys

To access USPS Rates, please press the CARRIER key then enter.  After pressing the Carrier key, follow the prompts to select the different shipping options.

*please note, by pressing the up and down arrow key, you can access additional shipping options such as Library, media, International, and more.

1st Class– Activating this function allows the selection of 1st Class.

Priority- Activating this function allows the selection of Priority mail.

Standard - This Activating this function allows Standard Single Piece and the Standard Parcel Post /Intra BMC or Inter BMC rate.

BPM- Activating this function allows Bound Print Matter rates.

Automation- Activating this function allows the selection of Automation rates.

Media- Activating this function allows the selection Media mail rates

Library - Activating this function allows Special Fourth Class Library rate.

Express - Activating this function allows the selection of Express Post Office to Addressee (PO-ADR) rate.

International (Surface & Air) - Activating this function allows the selection of either the International Air rates or the International Surface rates.

- International Air - This key is used to select the International Air rates. If an International Surface rate is already displayed, this key toggles the display to show the International Air rate.

- International Surface - This key is used to select the International Surface rates. If an International Air rate is already displayed, this key toggles the display to show the International Surface rate.

- Letter - This key is used to select the International Air Letter and Letter Packages rate.

- Parcel Post - This key is used to select the International Air or Surface Parcel Post rate.

- Small Packet/Printed Matter - This key is used to select the International Air or Surface Small Packet/Printed Matter rate.

- Canada (5) - This key is used to select Canada as the destination country whenever the scale is prompting for a country code. This key is also used as the numeric 5 key when numeric entry is required.

- Mexico (6) - This key is used to select Mexico as the destination country whenever the scale is prompting for a country code. This key is also used as the numeric 6 key when numeric entry is required.

      - UPS (United Parcel Service) Rate Keys

To access USPS Rates, please press the CARRIER key then enter.  After pressing the Carrier key, follow the prompts to select the different shipping options.

Next Day/Next Day/Next Day Saver- Activating this function allows the selection of either     Next Day/Next Day/Next Day Saver.  After making the selection, you will be prompt to select the type of package.  You will then need to select your designation zip code.  Many shipping options will be displayed after you have entered the required zip code.  These options included but not limited to COD, Delivery Confirmation, Signature confirmation, Insurance, Saturday Delivery and many more.

2nd Day Am - Activating this function allows the selection of 2nd Day Am.  After making the selection, you will be prompt to select the type of package.  You will then need to select your designation zip code.  Many shipping options will be displayed after you have entered the required zip code.  These options included but not limited to COD, Delivery Confirmation, Signature confirmation, Insurance, Saturday Delivery and many more.

2nd day/Ground/3 Day- These rates can be found with the up and down arrow keys after you have pressed the CARRIER key.  Activating this function allows the selection of either 2nd day/Ground/3 Day rates.  After making the selection, you will be prompt to select the type of package.  You will then need to select your designation zip code.  Many shipping options will be displayed after you have entered the required zip code.  These options included but not limited to COD, Delivery Confirmation, Signature confirmation, Insurance, Saturday Delivery and many more.

      - FedEx (Federal Express) Rate Keys

To access USPS Rates, please press the CARRIER key then enter.  After pressing the Carrier key, follow the prompts to select the different shipping options.

First/Standard/Priority/Eco 2Day rats- Activating this function allows the selection of either First/Standard/Priority/Eco 2Day rates.  After making the selection, you will be prompt to select the type of package.  You will then need to select your designation zip code.  Many shipping options will be displayed after you have entered the required zip code.  These options included but not limited to Insurance, Signature Confirmation and Delivery Confirmation.

3.2.2	OPERATOR KEYS

The remainder of the keys acts as various function keys.  Some have to do with rate calculations and some have to do with actual scale operation. In each case, pressing the key will activate the chosen function or prompt for further information.

3.2.2.1	SPECIAL SERVICES KEYS

These keys are used to select the special services for each carrier.   These special Service Keys are available after you have selected the CARRIER, type of package, and designated zip code.

- Certified - If this service is selected, the appropriate fee for the transaction is applied to the displayed rate.

- Collect On Delivery (C.O.D.) - If this service is selected, the scale displays “Enter Value ? _____.  Once the value is entered, the appropriate fee for the transaction is applied to the displayed rate.

- Insurance - If this service is selected, the scale displays “Enter Value ?_____    and allows you to enter the insured amount. After an amount is entered the appropriate fee for the transaction is applied to the displayed rate.

- Special Delivery – Such as Saturday delivery.  If this service is selected, the appropriate fee for the transaction is applied to the displayed rate.

- Signature confirmation/delivery confirmation- If this function is activated, the appropriate charges will be applied to the total cost of delivery.

3.2.2.2	SETUP KEY

The SETUP KEY (then pressing the Org ZIP key) is used to change the current ZIP code or zone. If three digits are entered, the scale assumes a new ZIP code has been entered. If a one or two digit code has been entered using the ENTER key, the scale assumes a new zone has been entered.  You can also access other functions such as the Beeper, remote weighing platform, as well as the F1 key configurations/options.

3.2.2.3	CLEAR KEY

The CLEAR/RESET key is used to clear the current entry, clear the special service fees applied. If an incorrect data entry is made, pressing this key will only clear the current data from the display.

3.2.2.4	ZERO KEY

The ZERO key is used to Zero the scale. When this key is selected, the scale zeros the weight.

3.2.2.5	ENTER KEY

The ENTER key is used to accept data when in data entry.

3.2.3	   FUNCTION KEYS

The function keys are used to access less frequently used scale operations.

3.2.3.1	STAR (*) KEY

The STAR (*) key is used to briefly display the actual rate charged by the carrier selected. This is used in conjunction with the handling charge feature described in section 6.2.2.

3.2.3.2	PIECE COUNT

The Piece Count function puts the scale into a counting mode.  Refer Section 5.1 for the Piece Count Operation procedure. Note that the counting mode is not available for legal for trade applications.

3.2.3.3 	DIMS KEY

When the DIMS key is pressed, the scale will prompt the user to enter the dimensions in    inches; there are three prompts: one for length, one for width and one for height.

3.2.3.4	 CLR KEY

You can always press the CLR hard key to return to the ‘Home’ screen

3.2.3.5	F1 Key

This key is used to access remote weighing benches.

3.3	GENERAL SCALE OPERATION

3.3.1	SYSTEM PROMPTS

The SPS-70DL scale prompts for information in two ways.

- Numeric Entry - This type of prompt appears as an “Enter Val” message with an equal sign indicating a zero value. Use the numeric keys to enter the requested data and press the ENTER key to complete the entry.  If you make a mistake during the entry, press the CLEAR key to start over.

- ZIP Code/ Country Code Entry - This type of prompt appears as a message with three dash marks ___.  Use the numeric keys to enter the requested data. There is no need to press the ENTER key to complete the entry.  If you make a mistake during the entry, press the CLEAR key to start over.

3.3.2	MAILING OR SHIPPING AN ITEM

There are four basic steps to shipping a letter or package. Refer to Section 4 for detailed examples.

1.	Place the letter or package on the scale’s platter and allow the weight indication to stabilize.  For more information on weighing an item, see Section 3.3.3.

2.	Press CARRIER key for mailing or shipping method.  Refer to Section 3.3.4 for more information on selecting the desired class of mail.

3.	If the method of shipment and/or the weight of the item requires a ZIP Code or country code, the scale prompts (displays three question marks) for a three digit code.  Use the numeric keys to enter the destination ZIP Code or country code.  Refer to Section 3.3.5.1 for more detailed information on entering a ZIP Code or Section 3.3.5.2 for more detailed information on entering a country code.

Please note:

The 70DL scale allows the user to select the country from a list if they don’t know the country; simply hit the “ListAll” soft key.

The 70DL scale allows the user to select the country from a favorites list which the user programs themselves; simply hit the “Favorites” soft key.

4.	If required, select a special service (i.e. Insurance, C.O.D., etc.).  Press the appropriate key to select the desired special service. Refer to Section 3.3.6 for more detailed instructions on the special services keys.

3.3.3	WEIGHING A LETTER OR PACKAGE

Before weighing an item, make sure the scale shows a zero weight indication.  If it does not, remove all items from the platter and press the ZERO key.

To weigh an item, place it on the center of the weighing platter.  Once the weight stabilizes, the scale’s display also stabilizes. If the item weight exceeds the scale’s weight capacity, it displays “OVERWT”.

3.3.4	SELECTING A CLASS OF SERVICE

To select a mailing or shipping rate, simply press the appropriate rate key. The available rates are listed in Section 3.2.1.

3.3.5   ENTERING A ZIP CODE OR COUNTRY CODE

      - ZIP CODE ENTRY

*There are two methods to select a country. Enter the three-digit numeric country code or select the country from a list.

There are 2 ways to select a country from a list:

- List All – This selection lists all countries on the screen in alphabetical order. Press the up/down arrow key to page up or down. Press and Hold the up /down arrow key to quickly scroll through the entire list. Press a soft key to select the desired country. A sample country list is shown in figure 2.

| INTL COUNTRY Country Code: |
| --- |
| Afganis | Algeria |
| Albania | Andora |

Figure 2

- Favorites – This selection displays an alphabetical user created list of countries. The user may add up to 32 countries to this list. Press the up/down arrows to page up or down. Press and Hold the up /down arrow key to quickly scroll through the entire list. Press a soft key to select the desired country.  Please see section 5.2 for detailed instructions.

3.3.6	SELECTING SPECIAL SERVICES

After selecting a rate, the scale will prompt you to select SPECIAL SERVICE. Selecting one or all the SPECIAL SERVICE keys will prompt the scale to calculate the shipping rate plus the SPECIAL SERVICE rates.

*When a value must be entered to determine the special service fee (COD, Registered, and Insurance), the scale prompts for a numeric entry.  After the amount is entered, press the ENTER key to accept the input.

# CHAPTER 4: EXAMPLES OF OPERATION

4.1	SENDING A LETTER OR PARCEL BY USPS FIRST CLASS/PRIORITY MAIL

1.	1ST Class Mail (Weight Less Than or Equal To 11 ounces)

| ACTION | DISPLAY EXAMPLE |
| --- | --- |
| Press the CARRIER key. Select USPS and then press enter. Select Letter, and then press enter. No further action is necessary. |  |

2.	Priority Mail (Weight from 1 Pound to 5 Pounds)

| ACTION | DISPLAY EXAMPLE |
| --- | --- |
| Press the CARRIER key. Select USPS and then press enter. Select Priority, and then press enter. Select the corresponding package size. Next, enter the destination country code. No further action is necessary. |  |

3.	Priority Mail (Over 5 Pounds)

| ACTION | DISPLAY EXAMPLE |
| --- | --- |
| Press the CARRIER key. Select USPS and then press enter. |  |
| Enter the type of packaging. |  |
| The screen now shows the USPS Priority Mail rate as well as Special Options such as Insurance, Certified, delivery confirmation, etc. |  |

4.2	SENDING AN INTERNATIONAL AIR LETTER BY USPS

| ACTION | DISPLAY EXAMPLE |
| --- | --- |
| Press the CARRIER key. Select USPS and then press enter. Press the down arrow until you see Intl option. |  |
| Using the arrow key, select the appropriate delivery service. After making your selection, choose the appropriate package format (Flat, Parcel or Letter). You will then need to enter the destination country code. |  |
| After selecting the country code, your rates will be displayed with Special delivery options. |  |

4.3	SENDING A LETTER BY UPS SECOND DAY AIR

| ACTION | DISPLAY EXAMPLE |
| --- | --- |
| Press the CARRIER key. Select UPS and then press enter. Press the down arrow until you see 2nd day option, select and press enter. |  |
| After you have selected the 2nd day air option, you will be asked to select the appropriate package size (Commercial Letter/Parcel or Residential Letter/Parcel. |  |
| The Scale will now ask you for the destination zip code. |  |
| After selecting the country code, your rates will be displayed with Special delivery options. |  |

4.4	SENDING A LETTER BY FEDERAL EXPRESS STANDARD OVERNIGHT

| ACTION | DISPLAY EXAMPLE |
| --- | --- |
| Press the CARRIER key. Select FEDEX and then press enter. Press the Standard option. |  |
| Select the appropriate package size. |  |
| The Scale will now ask you for the destination zip code. |  |
| After selecting the country code, your rates will be displayed with Special delivery options. |  |

# CHAPTER 5: ADVANCED FEATURES AND OPERATION

5.1    PROGRAMABLE SHORT CUT KEY

The scale contains 10 programmable shortcuts which are little macros used to save user keystrokes. The shortcuts are stored and retrieved by using the
numeric keys 0-9.

All 10 must be shared among the three postal carriers (USPS, UPS and FedEx).  To use a shortcut, the user must first switch to the right carrier.

*Out of the box, none of the shortcuts are programmed. The user must keep track of each shortcut programmed - maybe we should include a chart in the user guide which the user can use to write in the details?

NOTE: Before starting, the scale must be at its HOME screen and at zero; you must also determine which numeric key you will use to store the shortcut under, e.g. #1, #2, etc.

5.1.1   How to program Short Cuts

- Remove all items from the scale and press the ZERO hard key.

- Press and hold the CLR hard key until you hear double beep at which point you can release the key

- Switch to the proper carrier, e.g. USPS, UPS or FedEx

- Select the class of mail and (if desired) special services

- Press and hold a numeric key => when you hear the double beep and the screen says "Shortcut Saved" you may release the numeric key

    - How to Run  the Short Cut

- Switch to the proper carrier, e.g. USPS, UPS or FedEx

2. 	Press the numeric key you saved the shortcut under => scale automatically
      runs the shortcut and prompts you for any additional information as needed.

    - How to delete the Short Cut

- Navigate to the HOME screen by pressing and holding the CLR hard key until you hear the double beep.

- Press and hold the numeric key (pertaining to the shortcut you wish to
erase) until you hear the double beep => when you hear the double beep and
the screen says "Shortcut Saved" you may release the numeric key.

5.2     How to Add and Remove Countries from the Favorites List

5.2.1   ADD a country to the Favorites List

- Place an item on the scale and select an International class of mail.

- Select the List All soft key.

- Use the up/down arrows to scroll to the country to be added.

- Press and Hold the soft key next to the country to be added.

- The scale will prompt “Country Saved” then return to the list.

    - DELETE a country from the Favorites List

- Place an item on the scale and select an International class of mail.

- Select the Favorites soft key.

- Use the up/down arrows to scroll to the country to be deleted.

- Press and Hold the soft key next to the country to be deleted.

- The scale will prompt “Country Deleted” then return to the list.

5.3	PIECE COUNTING

This function is used to count items of identical weight.  To maintain the count accuracy, the following guidelines should be followed.

- All items placed on the scale must be of the same weight.

- The minimum sample count is 10.

- The minimum weight per piece must be 0.2 ounces for a sample count of 10.

- The total weight of the items sampled must be 2 ounces or greater.

- Remove all items from the scale.

- Press the ZERO key.

- Press the PIECE COUNT key. The scale prompts you to place a 10-piece sample count on the scale.

- Place the 10 piece sample count on the scale. The scale prompts you to press the ENTER key.

- Press the ENTER key.

- Remove the sample count from the scale.

- Place the items to be counted on the scale.  As items are added to or removed from the scale the display reflects count.

- Press the CLEAR key to return to normal scale operation.

NOTE: If the total weight of 10 samples is less than 2 ounces, it will not register as a full sample. If this occurs, press the ENTER key and the scale will prompt for a 20-piece sample count.

5.4	HOLD MODE OPERATION

- Remove all items from scale

- Press F1 hard key

- Press Hold soft key (Note: must be switched ON in Setup mode)

- Place oversize item onto scale. when scale beeps you may remove the

item and perform necessary rating functions.

- When done with hold mode, press the CLR hard key to exit back to

normal mode

NOTE: There is a 5 oz minimum weight limit for this function.

# CHAPTER 6: SETUP OPERATION

6.1	SETUP OPERATION OVERVIEW

The system setup consists of three setup areas: Configure Service, and Rate Table.

6.2	CONFIGURE MENU

The Configure Menu is used to configure the Origination ZIP code, Remote Scale, F1 Configure and Buzzer setup.  To access this menu, simply press the SETUP button.

6.2.1	ORIGINATION ZIP CODE

This function is used to program your origination ZIP code.

1.	Enter the Configure Menu Mode as described above.  Then press the arrow that points to the Configure option.

2.	The Screen should now display the following options:  Org ZIP, F1, Beeper, and Remote.  Press the arrow pointing to Org Zip.

3.	Using the numeric keys, enter the first three digits of your ZIP code. Once all three digits are entered, the scale prompts” ZIP Code OK?” and displays the current ZIP code. Repeat Step 2.

6.2.2	HANDLING CHARGE

This function is used to program a percentage markup for each major class of mail or carrier. In each case, you may enter a number from 0 to 99, with “0” indicating no markup and “99” indicating a 99% markup (1.99 times the true rate). The scale is shipped from the factory with all rates set to a 0% markup.

The rate categories available for markup include the following:

- First Class Single Piece (1ST)

- Priority Mail (PM)

- Standard Mail Single Piece (SMSP)

- Standard Mail Parcel Post (SMPP)

- INT’L Air/Surf (INTL)

- Library/Book (LIB)

- Express Mail (EXP)

- UPS Ground Com/Res (UPS GRD)

- UPS 2nd Day/Next Day (UPS AIR)

- All FedEx (FDX)

1.	Enter the Setup Menu Mode as described above and press ENTER (Yes) for current ZIP code. The scale prompts ” 1ST PERCENT OK?” and displays the current markup percentage.

2.	Press the ENTER (Yes) key to accept the displayed markup percentage for displayed rate category or press the CLEAR (No) key to change the markup percentage.

Note:  If “Yes” is selected, the scale proceeds to the next rate category listed above.  If “No” is selected, the message “Input PCT = ??” appears in the display.

3.	Using the numeric keys, enter the desired markup percentage. The scale asks if the percent markup for the displayed rate category is OK. Repeat Step 2.

Note:  If the desired markup percentage is less than 10, you must press the ENTER key. Otherwise, if the desired markup percentage is 10 or greater, the scale automatically enters the value for you.

4.	Repeat Steps 2 and 3 for all rate categories listed.

6.2.3	BUZZER ENABLE/DISABLE

Enter the Configure Menu Mode as described above.  Then press the arrow that points to the Configure option.

2.	The Screen should now display the following options:  Org ZIP, F1, Beeper, and Remote.  Press the arrow pointing to Beeper.

3.	Using the arrow keys, you may toggle the Beeper  to the on/off position.

6.3	CALIBRATION MENU

Calibration can only be performed by authorized Transcell Service personnel.

*For authorized service personnel, the calibration can be access via the SETUP menu.  You will need to obtain a Password from Transcell in order to calibrate the scale.

  - ANALOG TO DIGITAL CONVERSION (ADC) DIAGNOSTIC MENU

The ADC diagnostic menu can only be performed by authorized Transcell Service personnel.

*For authorized service personnel, the calibration can be access via the SETUP menu.  You will need to obtain a Password from Transcell in order to calibrate the scale.

# CHAPTER 7: LEGAL FOR TRADE SEALING

7.1	SEALING METHOD

The SPS-70DL scale only can be sealed for commercial (Legal for Trade) applications as follows.

- Turn the scale off.

- On the back of the scale, locate the Calibration Slide Switch Cover Plate (see illustration below).

- Remove the cover plate to reveal the Calibration Slide Switch.

- Turn the switch to the opposite position.

- Replace the slide switch cover and thread a wire security seal through both drilled head screws securing the calibration switch cover.

Figure 7-1: SPS-70DL Back Panel

# APPENDIX A: SPECIFICATIONS

| CAPACITY: 0–4 lb x 0.1 oz (SPS-70) 0–4 lb x 0.2 oz (SPS-150) 4–70 lb x 0.5 oz (SPS-70) 4–150 lb x 0.5 oz (SPS-150) CONSTRUCTION: Housings: Gray ABS Sub-Platform: Metal Platter: Stainless Steel Feet: Non-skid Hard Rubber DISPLAY: 16 x 2 Alpha, Liquid Crystal KEYPAD: 34-key Tactile Keypad OVER CAPACITY ANNUNCIATION: 103% of Full Scale Capacity | NON-LEGAL-FOR-TRADE OPERATING TEMPERATURE RANGE: 32F to 104F (0°C to 40°C) LEGAL-FOR-TRADE OPERATING TEMPERATURE RANGE: 41F to 95F (5°C to 35°C) POWER SOURCE: AC Adapter, 12VDC, 800 mA, included SERIAL PORT: Full Duplex RS-232, Male DSUB9 WEIGHT: Net Weight: 23.0 lb (10.4 kg) Shipping Weight: 24.0 lb (10.8 kg) |
| --- | --- |

PHYSICAL DIMENSIONS:

# APPENDIX B: STANDARD RATES, SPECIAL SERVICES AND FUNCTIONS

B.1	STANDARD RATES, SPECIAL SERVICES AND FUNCTIONS

B.1.1	UNITED STATES POSTAL SERVICE (USPS)

- 1st/Priority (Power On Default)

- Express PO-ADR

- Standard

- Book

- International

Air - Letter, Printed Matter, Small Packets, Parcel Post

Surface - Printed Matter, Small Packets, Parcel Post

- Library

B.1.2	UNITED PARCEL SERVICE (UPS)

- Next Day Air Letter/Package

- 2nd Day Air Letter/Package

- Ground Package Commercial/Residential

B.1.3	FEDERAL EXPRESS

- Priority Overnight Letter/Package

- Standard Overnight Letter/Package

- Economy 2 Day Letter/Package

B.1.4	SPECIAL SERVICES

- Registered with Insurance

- Registered without Insurance

- Insurance

- Collect On Delivery (COD)

- Return Receipt

- Certified

- Special Delivery

B.1.5	FUNCTIONS

- Clear

- Enter

- ZIP Code Origin

- Piece Count

- Special Services

- Zero Scale

- Handling Charge

# APPENDIX C: RATE AND SPECIAL SERVICE ABBREVIATIONS

C.1	RATE ABBREVIATIONS

| Rate | Display Abbreviation. |
| --- | --- |
| USPS First 1st Class (<11 oz) | 1ST |
| USPS 1st Priority (>11 oz) | PRI |
| USPS Express PO-ADR | EXP |
| USPS Standard Single Piece (<16 oz) | STD |
| USPS Standard Parcel Post (>16 oz) | STD |
| USPS Book | BOOK |
| USPS Library | LIB |
| USPS International Air Letter | AIR LETTER |
| USPS International Air Printed Matter | AIR PRT MATT |
| USPS International Air Parcel Post | AIR PARCEL |
| USP International Surface Printed Matter | SUR PRT MATT |
| USPS International Surface Parcel Post | SUR PARCEL |
| UPS Next Day Air Letter | NXT DAY LET |
| UPS Next Day Air Package | NXT DAY |
| UPS 2nd Day Air Letter | 2ND DAY LET |
| UPS 2nd Day Air Package | 2ND DAY |
| UPS Ground Commercial | GRD COM |
| UPS Ground Residential | GRD RES |
| Fed Ex Priority Letter | FDX PRI LET |
| Fed Ex Priority Package | FDX PRI |
| Fed Ex Standard Letter | FDX STD LET |
| Fed Ex Standard Package | FDX STD |
| Fed Ex Economy 2 Day Letter | FDX ECO LET |
| Fed Ex Economy 2 Day Package | FDX ECO |

C.2	SPECIAL SERVICES ABBREVIATONS

| Special Services Description | Long Display Abbreviation | Short Display Abbreviation |
| --- | --- | --- |
| Cash On Demand (COD) | COD | CO |
| Certified | CERT | CT |
| Insurance | INS | IN |
| Registered w/ postal insurance | REG (I) | RG |
| Registered w/o postal insurance | REG | RG |
| Return Receipt | RT RCPT | RR |
| Special Delivery | SP DLVY | SD |

# APPENDIX D: COUNTRY CODE CHART

TRANSCELL USPS INTERNATIONAL COUNTRY CODE CHART

*The 70DL scale allows the user to select the country from a list if they don’t know the country; simply hit the “ListAll” soft key.

*The 70DL scale allows the user to select the country from a favorites list which the user programs themselves; simply hit the “Favorites” soft key.

200 Afghanistan

201 Albania

202 Algeria

203 Andorra

204 Angola

205 Anguilla

206 Antigua & Barbuda

207 Argentina

208 Armenia

209 Aruba

210 Ascension

211 Australia

212 Austria

213 Azerbaijan

214 Azores

215 Bahamas

216 Bahrain

217 Bangladesh

218 Barbados

219 Belarus

220 Belgium

221 Belize

222 Benin

223 Bermuda

224 Bhutan

225 Bolivia

226 Bosnia-Herzegovina

227 Botswana

228 Brazil

229 British Virgin Islands

230 Brunei Darussalam

231 Bulgaria

232 Burkina Faso

233 Burma

234 Burundi

235 Cambodia

236 Cameroon

237 Canada

238 Cape Verde

239 Cayman Islands

240 Central African Republic

241 Chad

242 Chile

243 China

244 Colombia

245 Comoros

246 Congo, Republic of

413 Congo, Dem. Republic of

247 Corsica

248 Costa Rica

249 Cote d’Ivoire (Ivory Coast)

250 Croatia

251 Cuba

252 Cyprus

253 Czech Republic

254 Denmark

255 Djibouti

256 Dominica

257 Dominican Republic

258 Ecuador

259 Egypt

260 El Salvador

261 Equatorial Guinea

262 Eritrea

263 Estonia

264 Ethiopia

265 Falkland Islands

266 Faroe Island

267 Fiji

268 Finland

269 France, Monaco

270 French Guiana

271 French Polynesia

272 Gabon

273 Gambia

274 Rep. of Georgia

275 Germany

276 Ghana

277 Gibraltar

278 Great Britain/North Ireland

279 Greece

280 Greenland

281 Grenada

282 Guadeloupe

283 Guatemala

284 Guinea

285 Guinea-Bissau

286 Guyana

287 Haiti

288 Honduras

289 Hong Kong

290 Hungary

291 Iceland

292 India

293 Indonesia

294 Iran

295 Iraq

296 Ireland (Eire)

297 Israel

298 Italy

299 Jamaica

300 Japan

301 Jordan

302 Kazakhstan

303 Kenya

304 Kiribati

305 Korea, North

306 Korea, South

307 Kuwait

308 Kyrgyzstan

309 Laos

310 Latvia

311 Lebanon

312 Lesotho

313 Liberia

314 Libya

315 Liechtenstein

316 Lithuania

317 Luxembourg

318 Macao

319 Macedonia

320 Madagascar

321 Madeira Island

322 Malawi

323 Malaysia

324 Maldives

325 Mali

326 Malta

327 Martinique

328 Mauritania

329 Mauritius

330 Mexico

331 Moldova

332 Mongolia

333 Montserrat

334 Morocco

335 Mozambique

336 Namibia

337 Nauru

338 Nepal

339 Netherlands

340 Netherlands Antilles

341 New Caledonia

342 New Zealand

343 Nicaragua

344 Niger

345 Nigeria

346 Norway

347 Oman

348 Pakistan

349 Panama

350 Papua New Guinea

351 Paraguay

352 Peru

353 Philippines

354 Pitcairn Island

355 Poland

356 Portugal

357 Qatar

358 Reunion

359 Romania

360 Russia

361 Rwanda

362 St. Christopher & Nevis

363 St. Helena

364 St. Lucia

365 St. Pierre & Miquelon

366 St. Vincent & Grenadines

367 San Marino

368 Sao Tome & Principe

369 Saudi Arabia

370 Senegal

371 Serbia-Montenegro

372 Seychelles

373 Sierra Leone

374 Singapore

375 Slovak Republic

376 Slovenia

377 Solomon Islands

378 Somalia

379 South Africa

380 Spain

381 Sri Lanka

382 Sudan

383 Suriname

384 Swaziland

385 Sweden

386 Switzerland

387 Syrian Arab Republic

388 Taiwan

389 Tajikistan

390 Tanzania

391 Thailand

392 Togo

393 Tonga

394 Trinidad & Tobago

395 Tristan Da Cunha

396 Tunisia

397 Turkey

398 Turkmenistan

399 Turks & Caicos Islands

400 Tuvalu

401 Uganda

402 Ukraine

403 United Arab Emirate

404 Uruguay

405 Uzbekistan

406 Vanuatu

407 Vatican City

408 Venezuela

409 Vietnam

410 Wallis & Futuna Islands

411 Western Samoa

412 Yemen

414 Zambia

415 Zimbabwe

# APPENDIX E: COUNTRY NAME ABBREVIATIONS

| Country Name | Abbr. |  | Country Name | Abbr. |
| --- | --- | --- | --- | --- |
| Afghanistan | AFGHANIS |  | Cuba | CUBA |
| Albania | ALBANIA |  | Cyprus | CYPRUS |
| Algeria | ALGERIA |  | Czech Republic | CZECH RE |
| Andorra | ANDORRA |  | Denmark | DENMARK |
| Angola | ANGOLA |  | Djibouti | DJIBOUTI |
| Anguilla | ANGUILLA |  | Dominican Republic | DOM REP |
| Antigua & Barbuda | ANTIGUA |  | Dominica | DOMINICA |
| Argentina | ARGENTIN |  | Ecuador | ECUADOR |
| Armenia | ARMENIA |  | Egypt | EGYPT |
| Aruba | ARUBA |  | El Salvador | EL SALVA |
| Ascension | ASCENSIO |  | Equatorial Guinea | EQUATORI |
| Australia | AUSTRALI |  | Eritrea | ERITREA |
| Austria | AUSTRIA |  | Estonia | ESTONIA |
| Azerbaijan | AZERBAIJ |  | Ethiopia | ETHIOPIA |
| Azores | AZORES |  | Falkland Islands | FALKLAND |
| British Virgin Isles | VIRGIN I |  | Faroe Islands | FAROE IS |
| Bahamas | BAHAMAS |  | Fiji Islands | FIJI |
| Bahrain | BAHRAIN |  | Finland | FINLAND |
| Bangladesh | BANGLADE |  | France, Monaco | FRANCE |
| Barbados | BARBADOS |  | French Guiana | FRENCH G |
| Belarus | BELARUS |  | French Polynesia | FRENCH P |
| Belgium | BELGIUM |  | Gabon | GABON |
| Belize | BELIZE |  | Gambia | GAMBIA |
| Benin | BENIN |  | Republic of Georgia | GEORGIA |
| Bermuda | BERMUDA |  | Germany | GERMANY |
| Bhutan | BHUTAN |  | Ghana | GHANA |
| Bolivia | BOLIVIA |  | Gibraltar | GIBRALTA |
| Bosnia-Herzegovina | BOSNIA-H |  | Great Britain/North Ireland | GREAT BR |
| Botswana | BOTSWANA |  | Greece | GREECE |
| Brazil | BRAZIL |  | Greenland | GREENLAN |
| Brunei Darussalam | BRUNEI D |  | Grenada | GRENADA |
| Bulgaria | BULGARIA |  | Guadeloupe | GUADELOU |
| Burkina Faso | BURKINA |  | Guatemala | GUATEMAL |
| Burma | BURMA |  | Guinea-Bissau | GUINEA- |
| Burundi | BURUNDI |  | Guinea | GUINEA |
| Central African Republic | CENT AFR |  | Guyana | GUYANA |
| Cambodia | CAMBODIA |  | Haiti | HAITI |
| Cameroon | CAMEROON |  | Honduras | HONDURAS |
| Canada | CANADA |  | Hong Kong | HONG KON |
| Cape Verde | CAPE VER |  | Hungary | HUNGARY |
| Cayman Islands | CAYMAN I |  | Iceland | ICELAND |
| Chad | CHAD |  | India | INDIA |
| Chile | CHILE |  | Indonesia | INDONESI |
| China | CHINA |  | Iran | IRAN |
| Colombia | COLOMBIA |  | Iraq | IRAQ |
| Comoros | COMOROS |  | Ireland (Erie) | IRELAND |
| Congo, Dem. Republic of | CONGO DE |  | Israel | ISRAEL |
| Congo, Republic of | CONGO RE |  | Italy | ITALY |
| Corsica | CORSICA |  | Ivory Coast | COTE D'L |
| Costa Rica | COSTA RI |  | Jamaica | JAMAICA |
| Croatia | CROATIA |  | Japan | JAPAN |
| Jordan | JORDAN |  | Philippines | PHILIPPI |
| Kazakhstan | KAZAKHST |  | Pitcairn Islands | PITCAIRN |
| Kenya | KENYA |  | Poland | POLAND |
| Kiribati | KIRIBATI |  | Portugal | PORTUGAL |
| Kuwait | KUWAIT |  | Qatar | QATAR |
| Kyrgyzstan | KYRGYZST |  | Reunion | REUNION |
| Laos | LAOS |  | Romania | ROMANIA |
| Latvia | LATVIA |  | Russia | RUSSIA |
| Lebanon | LEBANON |  | Rwanda | RWANDA |
| Lesotho | LESOTHO |  | South Africa | SOUTH AF |
| Liberia | LIBERIA |  | South Korea | KOREA RE |
| Libya | LIBYA |  | Sierra Leone | SIERRA L |
| Liechtenstein | LIECHTEN |  | San Marino | SAN MARI |
| Lithuania | LITHUANI |  | Sao Tomes & Principe | SAO TOME |
| Luxembourg | LUXEMBOU |  | Saudi Arabia | SAUDI AR |
| Macao | MACAO |  | Senegal | SENEGAL |
| Macedonia | MACEDONIA |  | Serbia-Montenegro | SERBIA-M |
| Madagascar | MADAGASC |  | Seychelles | SEYCHELL |
| Madeira Island | MADEIRA |  | Singapore | SINGAPOR |
| Malawi | MALAWI |  | Slovakia Republic | SLOVAK R |
| Malaysia | MALAYSIA |  | Slovenia | SLOVENIA |
| Maldives | MALDIVES |  | Solomon Islands | SOLOMON |
| Mali | MALI |  | Somalia | SOMALIA |
| Malta | MALTA |  | Spain | SPAIN |
| Martinique | MARTINIQ |  | Sri Lanka | SRI LANK |
| Mauritania | MAURITAN |  | St Christopher & Nevis | ST. CHRI |
| Mauritius | MAURITIU |  | St Lucia | SAINT LU |
| Mexico | MEXICO |  | St Pierre & Miquelon | SAINT PI |
| Moldova | MOLDOVA |  | St Helena | SAINT HE |
| Mongolia | MONGOLIA |  | St Vincent & Grenadines | SAINT VI |
| Montserrat | MONTSERR |  | Sudan | SUDAN |
| Morocco | MOROCCO |  | Suriname | SURINAME |
| Mozambique | MOZAMBIQ |  | Swaziland | SWAZILAN |
| North Korea | KOREA DE |  | Sweden | SWEDEN |
| Namibia | NAMIBIA |  | Switzerland | SWITZERL |
| Nauru | NAURU |  | Syrian Arab Republic | SYRIA |
| Nepal | NEPAL |  | Taiwan | TAIWAN |
| Netherlands Antilles | NET ANTI |  | Tajikistan | TAJIKIST |
| Netherlands | NETHERLA |  | Tanzania | TANZANIA |
| New Caledonia | NEW CALE |  | Thailand | THAILAND |
| New Zealand | NEW ZEAL |  | Togo | TOGO |
| Nicaragua | NICARAGU |  | Tonga | TONGA |
| Niger | NIGER |  | Trinidad & Tobago | TRINIDAD |
| Nigeria | NIGERIA |  | Tristan Da Cunha | TRISTAN |
| Norway | NORWAY |  | Turkmenistan | TURKMENI |
| Oman | OMAN |  | Tunisia | TUNISIA |
| Pakistan | PAKISTAN |  | Turkey | TURKEY |
| Panama | PANAMA |  | Turks & Caicos | TURKS & |
| Papua New Guinea | PAPUA NE |  | Tuvalu | TUVALU |
| Paraguay | PARAGUAY |  | Uganda | UGANDA |
| Peru | PERU |  | Ukraine | UKRAINE |
| United Arab Emirate | UNITED A |
| Uruguay | URUGUAY |
| Uzbekistan | UZBEKIST |
| Vanuatu | VANUATU |
| Vatican City | VATICAN |
| Venezuela | VENEZUEL |
| Vietnam | VIETNAM |
| Wallis & Futuna Islands | WALLIS & |
| Western Samoa | W. SAMOA |
| Yemen | YEMEN |
| Zambia | ZAMBIA |
| Zimbabwe | ZIMBABWE |

# APPENDIX F: RATE CHANGE INFORMATION

F.1	RATE UPDATES

Transcell updates carrier rate and structure changes. The rates and operating system reside on one Rate Card, which is removable from the scale for reprogramming purposes.

- Turn the scale’s AC power switch to the off position.

- Remove the Rate Card cover from the right hand side of the scale.

- Install the Rate Card in the scale with the component side of the module facing the top of the scale.

Need new procedure

# APPENDIX G: ERROR MESSAGES

G.1	ERROR MESSAGES

If the scale encounters an error condition, it will display a message alerting the operator.  A description of each display follows:

G.1.1	OPERATOR ERRORS

| Message | Explanation |
| --- | --- |
| ovwt | Indicates that the weight for the class of service selected has been exceeded |
| underwt | Indicates that the weight for the class of service selected is too light |
| OVERWT | Indicates that the weighing capacity of the scale has been exceeded |
| – – – – – – – | Indicates that the weight reading is less than zero |
| Invalid Zip Code Invalid Zone # | Indicates that an invalid ZIP code or zone was entered |
| Invalid Cty Code | Indicates that an invalid country code was entered |
| Service N/A | Indicates that the special service is not valid for the class of mail selected |
| Invalid Service | Indicates that the special service is not valid with the current special service(s) selected. |

APPENDIX H:  RATE MATRIX

USPS: Rate map and explanation

|  | Soft keys | Main Display |
| --- | --- | --- |
| Class of Mail | Level 1 | Level 2 | Level 3 | Level 4 | Combined Text |
| Bound Printed Matter - Flats | BPM | Flat |  |  | BPM F |
| Bound Printed Matter - Parcels | BPM | Parcel |  |  | BPM P |
| Express Mail Intl | Intl | Express | Parcel |  | INT EMI |
| Express Mail Intl Flat-rate Envelope | Intl | Express | Envelope |  | INT EMI E |
| Express Mail | Express | Parcel |  |  | EXP |
| Express Mail Flat-rate Envelope | Express | Envelope |  |  | EXP E |
| First Class Flat | 1st Class | Flat |  |  | 1ST F |
| First Class Letter | 1st Class | Letter |  |  | 1ST L |
| First Class Parcel | 1st Class | Parcel |  |  | 1ST P |
| First Class Postcard | 1st Class | Postcard |  |  | 1ST C |
| First Class Intl Flat | Intl | First Class | Flat |  | INT FCI F |
| First Class Intl Letter | Intl | First Class | Letter |  | INT FCI L |
| First Class Intl Parcel | Intl | First Class | Parcel |  | INT FCI P |
| First Class Intl Postcard | Intl | Postcard |  |  | INT FCI C |
| First Class 5-Digit Letter | Automation | Letter | 5 Digit |  | AUT L 5DG |
| First Class 3-Digit Letter | Automation | Letter | 3 Digit |  | AUT L 3DG |
| First Class AADC Letter | Automation | Letter | AADC Let |  | AUT L AAD |
| First Class Mixed AADC Letter | Automation | Letter | MAADC Let |  | AUT L MIX |
| First Class Presorted Letter | Automation | Letter | Presorted |  | AUT L PRE |
| First Class 5-Digit Flat | Automation | Flat | 5 Digit |  | AUT F 5DG |
| First Class 3-Digit Flat | Automation | Flat | 3 Digit |  | AUT F 3DG |
| First Class ADC Flat | Automation | Flat | ADC |  | AUT F ADC |
| First Class Mixed ADC Flat | Automation | Flat | MADC |  | AUT F MIX |
| First Class Presorted Flat | Automation | Flat | Presorted |  | AUT F PRE |
| First Class 5-Digit Parcel | Automation | Parcel | 5 Digit |  | AUT P 5DG |
| First Class 3-Digit Parcel | Automation | Parcel | 3 Digit |  | AUT P 3DG |
| First Class ADC Parcel | Automation | Parcel | ADC |  | AUT P ADC |
| Global Express Guaranteed | Intl | GXG |  |  | INT GXG |
| Library Mail | Library |  |  |  | LIB |
| Media Mail | Media |  |  |  | MED |
| Parcel Post | Par Post |  |  |  | PP |
| Prioity Mail | Priority | Parcel |  |  | PRI |
| Priority Mail Flat-rate Small Box | Priority | Sm Box |  |  | PRI SB |
| Priority Mail Flat-rate Regular Box | Priority | Rg Box |  |  | PRI RB |
| Priority Mail Flat-rate Large Box | Priority | Lg Box |  |  | PRI LB |
| Priority Mail Flat-rate Envelope | Priority | Envelope |  |  | PRI E |
| Prioity Mail Intl | Int'l | Priority | Parcel |  | INT PMI |
| Prioity Mail Intl Flat-rate Small Box | Int'l | Priority | Sm Box |  | INT PMI SB |
| Prioity Mail Intl Flat-rate Regular Box | Int'l | Priority | Rg Box |  | INT PMI RB |
| Prioity Mail Intl Flat-rate Large Box | Int'l | Priority | Lg Box |  | INT PMI LB |
| Prioity Mail Intl Flat-rate Envelope | Int'l | Priority | Envelope |  | INT PMI E |
| Extra (Special) Service |  |  |  |  | Short Text |
| Balloon Rate |  |  |  |  | BL |
| Certified |  |  |  | Certified | CT |
| COD |  |  |  | COD | CO |
| Delivery Confirmation |  |  |  | Del Conf | DC |
| Dimensional Rate |  |  |  | Dims | DW |
| Insurance |  |  |  | Insurance | IN |
| Registered (international) |  |  |  | Regstd | RG |
| Registered (no insurance) |  |  |  | Regstd | RG |
| Registered (w/insurance) |  |  |  | Regstd | RG |
| Return Receipt |  |  |  | Ret Rcpt | RR |
| Return Receipt for Merchandise |  |  |  | RR Merch | RM |
| Signature Confirmation |  |  |  | Sig Conf | SC |
| Nonmachinable Surcharge (letters) |  |  |  | Oversize | OV |
| Sunday/Holiday Surcharge |  |  |  | Del Sur | DS |

UPS: Rate map and explanation

|  | Soft keys | Display |
| --- | --- | --- |
| Class of Mail | Level 1 | Level 2 | Level 3 | Level 4 | Combined Text |
| Commercial UPS Next Day Air Early A.M. Letter | Next AM | Com Let |  |  | NXT AM CL |
| Commercial UPS Next Day Air Early A.M. Package | Next AM | Com Pcl |  |  | NXT AM CP |
| Residential UPS Next Day Air Early A.M. Letter | Next AM | Res Let |  |  | NXT AM RL |
| Residential UPS Next Day Air Early A.M. Package | Next AM | Res Pcl |  |  | NXT AM RP |
| Commercial UPS Next Day Air Letter | Next Day | Com Let |  |  | NXT CL |
| Commercial UPS Next Day Air Package | Next Day | Com Pcl |  |  | NXT CP |
| Residential UPS Next Day Air Letter | Next Day | Res Let |  |  | NXT RL |
| Residential UPS Next Day Air Package | Next Day | Res Pcl |  |  | NXT RP |
| Commercial UPS Next Day Air Saver Letter | Next Saver | Com Let |  |  | NXT SV CL |
| Commercial UPS Next Day Air Saver Package | Next Saver | Com Pcl |  |  | NXT SV CP |
| Residential UPS Next Day Air Saver Letter | Next Saver | Res Let |  |  | NXT SV RL |
| Residential UPS Next Day Air Saver Package | Next Saver | Res Pcl |  |  | NXT SV RP |
| Commercial UPS 2nd Day Air A.M. Letter | 2nd AM | Com Let |  |  | 2ND AM CL |
| Commercial UPS 2nd Day Air A.M. Package | 2nd AM | Com Pcl |  |  | 2ND AM CP |
| Residential UPS 2nd Day Air A.M. Letter | 2nd AM | Res Let |  |  | 2ND AM RL |
| Residential UPS 2nd Day Air A.M. Package | 2nd AM | Res Pcl |  |  | 2ND AM RP |
| Commercial UPS 2nd Day Air Letter | 2nd Day | Com Let |  |  | 2ND CL |
| Commercial UPS 2nd Day Air Package | 2nd Day | Com Pcl |  |  | 2ND CP |
| Residential UPS 2nd Day Air Letter | 2nd Day | Res Let |  |  | 2ND RL |
| Residential UPS 2nd Day Air Package | 2nd Day | Res Pcl |  |  | 2ND RP |
| Commercial UPS 3 Day Select | 3 Day | Com Pcl |  |  | 3DY CP |
| Residential UPS 3 Day Select | 3 Day | Res Pcl |  |  | 3DY RP |
| Commercial UPS Ground | Ground | Com Pcl |  |  | GND CP |
| Residential UPS Ground | Ground | Res Pcl |  |  | GND RP |
| Extra (Special) Service |  |  |  |  | Short Text |
| COD |  |  |  | COD | CO |
| Delivery Confirmation |  |  |  | Del Conf | DC |
| Dimensional Rate |  |  |  |  | DW |
| Declared Value |  |  |  | Insurance | IN |
| Signature Confirmation |  |  |  | Sig Conf | SC |
| Saturday Delivery |  |  |  | Sat Del | SD |
| Additional Handling |  |  |  | Add Hand | AH |
| Delivery Surcharge |  |  |  | Del Sur | DS |

FEDEX: Rate map and explanation

|  | Soft keys | Display |
| --- | --- | --- |
| Class of Mail | Level 1 | Level 2 | Level 3 | Level 4 | Combined Text |
| Commercial FedEx First Overnight Letter | First | Com Let |  |  | 1ST CL |
| Commercial FedEx First Overnight Package | First | Com Pcl |  |  | 1ST CP |
| Residential FedEx First Overnight Letter | First | Res Let |  |  | 1ST RL |
| Residential FedEx First Overnight Package | First | Res Pcl |  |  | 1ST RP |
| Commercial FedEx Priority Overnight Letter | Priority | Com Let |  |  | PRI CL |
| Commercial FedEx Priority Overnight Package | Priority | Com Pcl |  |  | PRI CP |
| Residential FedEx Priority Overnight Letter | Priority | Res Let |  |  | PRI RL |
| Residential FedEx Priority Overnight Package | Priority | Res Pcl |  |  | PRI RP |
| Commercial FedEx Standard Overnight Letter | Standard | Com Let |  |  | STD CL |
| Commercial FedEx Standard Overnight Package | Standard | Com Pcl |  |  | STD CP |
| Residential FedEx Standard Overnight Letter | Standard | Res Let |  |  | STD RL |
| Residential FedEx Standard Overnight Package | Standard | Res Pcl |  |  | STD RP |
| Commercial FedEx 2 Day Letter | Eco 2Day | Com Let |  |  | ECO CL |
| Commercial FedEx 2 Day Package | Eco 2Day | Com Pcl |  |  | ECO CP |
| Residential FedEx 2 Day Letter | Eco 2Day | Res Let |  |  | ECO RL |
| Residential FedEx 2 Day Package | Eco 2Day | Res Pcl |  |  | ECO RP |
| Commercial FedEx Express Saver Letter | Exp Saver | Com Let |  |  | SAV CL |
| Commercial FedEx Express Saver Package | Exp Saver | Com Pcl |  |  | SAV CP |
| Residential FedEx Express Saver Letter | Exp Saver | Res Let |  |  | SAV RL |
| Residential FedEx Express Saver Package | Exp Saver | Res Pcl |  |  | SAV RP |
| Extra (Special) Service |  |  |  |  | Short Text |
| COD |  |  |  | COD | CO |
| Delivery Confirmation |  |  |  | Del Conf | DC |
| Dimensional Rate |  |  |  |  | DW |
| Declared Value |  |  |  | Insurance | IN |
| Signature Confirmation |  |  |  | Sig Conf | SC |
| Saturday Delivery |  |  |  | Sat Del | SD |
| Additional Handling |  |  |  | Add Hand | AH |
| Delivery Surcharge |  |  |  | Del Sur | DS |

Limited 12 month Warranty

This product is warranted by Transcell Technology against manufacturing defects in material and workmanship under normal use for twelve (12) months from the date of purchase. For complete warranty details and service information, please contact us at the address below.

Contents subject to change without notice.

Transcell Technology, Inc.

975 Deerfield Parkway

Buffalo Grove, IL 60089

Tel (847) 419-9180

Fax (847) 419-1515

Web: www.transcell.net